## Slide 1: Helicopter Flight Dynamics modelling with state-of-the-art dynamic inflow
Ioannis Karatsivoulis- Undergraduate Student, Department of Aeronautics, Imperial College London
Final Year Project (FYP)
04/03/2020
Interim presentation
04/03/2020

## Slide 2: Background
Final Year Project (FYP)
04/03/2020
CFD
Vortex Wake Models (VWM)
Dynamic wake (inflow)
Wake models
Free Wake Models (FWM)
Prescribed Wake Models (FWM)
Notes: Could potentially try the ground effect one Although no validation available due to lack of existing flight test data nor the wake model (ground effect is not modelled for ground effect– This is one of the newest version of the wake model).
Have clear understanding of what the model and equations are, where they fit in. Not need to have started/finished coding. Be very clear about the direction/meaning of the project. TALK ABOUT THE CODE (flight dynamics code-introduction in Dr Ribera’s paper). WAHAT IT DOES AND DOES NOT DO. NOT A CFD CODE. HOW THE CODE CAN HAVE DIFFERENT CODES AND MODELS TO CALCULATE THESE VELOCITIES, FROM FREE WAKE TO DYNAMIC INFLOW. EXPLAIN HOW INFLOW FITS IN THERE. SAY ABOUT PROGRESS OF THE MODEL. EXTENDING FLIGHT CONDITIONS CAPTURED THROUGH THE INFLOW MODELS. IDEA: ADD LATER VERSIONS OF CODE. ESPECIALLY THE VORTEX RING STATE; ACCORDING TO DR RIBERAS THESIS. Highlight bits you want people to read.
Feedback: Take the subroutines I have been sent, and start looking at how to the equations in the model correlate with the code. Start to match that and see how it will match your own implementation. See how the commented bit matches any vortex ring corrections. Ensure you understand how the theory matches the 2 sub-routines.

## Slide 3: CFD
Very powerful
Can solve almost anything
✖ Very computationally expensive
✖ Cannot solve turbulence
✖ Grid-dependent solution
Final Year Project (FYP)
04/03/2020

## Slide 4: Vortex Wake Models
Wake modelled as vortex lines
Discretized into lattice of vortex elements:
  Straight
  Curved
  Blobs
Two ways to describe transport of wake vorticity:
  Free wake: First principles
  Prescribed wake: - Wake filament position specified a priori
  - Approximate near-rotor velocity field
Final Year Project (FYP)
04/03/2020
Notes: ADD SOURCE.

## Slide 5: Vortex Wake Models
Once the position and strength of the wake vorticity are calculated, the Biot-Savart law is used to work out the induced velocity field at the rotor, followed by numerical integration
✖ Computationally expensive: High filament number for accurate wake
representation
Final Year Project (FYP)
04/03/2020
Notes: Could potentially try the ground effect one Although no validation available due to lack of existing flight test data nor the wake model (ground effect is not modelled for ground effect– This is one of the newest version of the wake model).
Have clear understanding of what the model and equations are, where they fit in. Not need to have started/finished coding. Be very clear about the direction/meaning of the project. TALK ABOUT THE CODE (flight dynamics code-introduction in Dr Ribera’s paper). WAHAT IT DOES AND DOES NOT DO. NOT A CFD CODE. HOW THE CODE CAN HAVE DIFFERENT CODES AND MODELS TO CALCULATE THESE VELOCITIES, FROM FREE WAKE TO DYNAMIC INFLOW. EXPLAIN HOW INFLOW FITS IN THERE. SAY ABOUT PROGRESS OF THE MODEL. EXTENDING FLIGHT CONDITIONS CAPTURED THROUGH THE INFLOW MODELS. IDEA: ADD LATER VERSIONS OF CODE. ESPECIALLY THE VORTEX RING STATE; ACCORDING TO DR RIBERAS THESIS. Highlight bits you want people to read.
Feedback: Take the subroutines I have been sent, and start looking at how to the equations in the model correlate with the code. Start to match that and see how it will match your own implementation. See how the commented bit matches any vortex ring corrections. Ensure you understand how the theory matches the 2 sub-routines.

## Slide 6: Dynamic Wake (Inflow) Models
Momentum (unsteady actuator disk) theory: change in aerodynamic forces across the rotor disk is responsible for creating a certain inflow distribution
Inflow treated as additional Degrees of Freedom
1st order ODE, state-space form
Final Year Project (FYP)
04/03/2020

## Slide 7: Dynamic Wake (Inflow) Models
Easily incorporated into flight dynamics codes (FLIGHTLAB, RCAS, HeliUM)
Computationally cheapest model
Potential for real-time simulation
Hierarchical improvement
✖ Linear model=> Problem with capturing non-linear effects
Final Year Project (FYP)
04/03/2020
Notes: Add: Modified/correlated to explain unexplained physical phenomena. Not absolutely based on first principles. Optimum around specific flight conditions

## Slide 8: Flight Conditions
No inflow model is perfect for all conditions
Flight condition ranking (wrt interest):
Descent  Vortex Ring State
Ground effect  Additional lift created
Manoeuvring flight Capturing wake skew, curvature and off-axis response
Final Year Project (FYP)
04/03/2020
Notes: Wrt= with respect to
ADD SOURCE

## Slide 9: The HeliUM code
Helicopter Flight Dynamics code
University of Maryland & NASA
Not CFD
Different wake models:
  Free-Wake
  Dynamic inflow
Accurate but slow=> NO real-time potential
Final Year Project (FYP)
04/03/2020
Notes: Have clear understanding of what the model and equations are, where they fit in. Not need to have started/finished coding. Be very clear about the direction/meaning of the project. TALK ABOUT THE CODE (flight dynamics code-introduction in Dr Ribera’s paper). WAHAT IT DOES AND DOES NOT DO. NOT A CFD CODE. HOW THE CODE CAN HAVE DIFFERENT CODES AND MODELS TO CALCULATE THESE VELOCITIES, FROM FREE WAKE TO DYNAMIC INFLOW. EXPLAIN HOW INFLOW FITS IN THERE. SAY ABOUT PROGRESS OF THE MODEL. EXTENDING FLIGHT CONDITIONS CAPTURED THROUGH THE INFLOW MODELS. IDEA: ADD LATER VERSIONS OF CODE. ESPECIALLY THE VORTEX RING STATE; ACCORDING TO DR RIBERAS THESIS. Highlight bits you want people to read.
Feedback: Take the subroutines I have been sent, and start looking at how to the equations in the model correlate with the code. Start to match that and see how it will match your own implementation. See how the commented bit matches any vortex ring corrections. Ensure you understand how the theory matches the 2 sub-routines.

## Slide 10: Aims and objectives
All analyses on the UH-60 Black Hawk
Find inflow model for a not-so-well-modelled condition
Code it inside the HeliUM flight dynamics code
Free wake data validation
Final Year Project (FYP)
04/03/2020
Notes: In the code, there are 2 inflow models, Pitt-Peters and Peters-he, which we are going to be modifying. We’ll be extended the extended models capture additional manoeuvres/flight regimes. Already in the code.

## Slide 11: Pitt-Peters (1980)
Excellent results in hover
: uniform; longitudinal, lateral
: gain matrix
: apparent mass matrix
: Time-constant matrix & Time lag
in the wake’s development
Based on Prandtl’s acceleration potential function: Satisfied the Laplace (potential flow) equation and gives a pressure discontinuity across the disc, leading the the creation of lift
Final Year Project (FYP)
04/03/2020
Notes: Could potentially try the ground effect one Although no validation available due to lack of existing flight test data nor the wake model (ground effect is not modelled for ground effect– This is one of the newest version of the wake model).
Have clear understanding of what the model and equations are, where they fit in. Not need to have started/finished coding. Be very clear about the direction/meaning of the project. TALK ABOUT THE CODE (flight dynamics code-introduction in Dr Ribera’s paper). WAHAT IT DOES AND DOES NOT DO. NOT A CFD CODE. HOW THE CODE CAN HAVE DIFFERENT CODES AND MODELS TO CALCULATE THESE VELOCITIES, FROM FREE WAKE TO DYNAMIC INFLOW. EXPLAIN HOW INFLOW FITS IN THERE. SAY ABOUT PROGRESS OF THE MODEL. EXTENDING FLIGHT CONDITIONS CAPTURED THROUGH THE INFLOW MODELS. IDEA: ADD LATER VERSIONS OF CODE. ESPECIALLY THE VORTEX RING STATE; ACCORDING TO DR RIBERAS THESIS. Highlight bits you want people to read.
Feedback: Take the subroutines I have been sent, and start looking at how to the equations in the model correlate with the code. Start to match that and see how it will match your own implementation. See how the commented bit matches any vortex ring corrections. Ensure you understand how the theory matches the 2 sub-routines.

## Slide 12: Pitt-Peters (1980)
✖ Can only go up to 2 harmonics
✖ For each harmonic, only 1 radial shape function used for the induced inflow
Final Year Project (FYP)
04/03/2020
Notes: Sources:
1. He’s PhD thesis: https://search.proquest.com/docview/303711620?pq-origsite=primo

## Slide 13: Peters-He (1989)
Slightly different 1st order ODE
Based on Potential flow functions by Prandtl & Kinner.
Advances made:
Inflow distribution expanded in terms of both harmonic and radial shape functions with undetermined coefficients. This expression can be up to 1000 harmonics
Complete description of radial inflow variation, consistent with, consistent with elastic blade modelling.
Final Year Project (FYP)
04/03/2020
Notes: Sources:
1. He’s PhD thesis: https://search.proquest.com/docview/303711620?pq-origsite=primo
In a helicopter, there is a retreating and advancing disk, which means that the rotor does not produce the same amount of lift for each azimuthal position. Consequently, since (by definition of the induced inflow theory) the inflow is a result of the lift, the blade will nto produce the same amount of inflow at each azimuthal location. As such, the inflow will vary sinusoidally/cosinusoidally

## Slide 14: Peters-He (1989)
Final Year Project (FYP)
04/03/2020
Notes: Sources:
1. He’s PhD thesis: https://search.proquest.com/docview/303711620?pq-origsite=primo
In a helicopter, there is a retreating and advancing disk, which means that the rotor does not produce the same amount of lift for each azimuthal position. Consequently, since (by definition of the induced inflow theory) the inflow is a result of the lift, the blade will nto produce the same amount of inflow at each azimuthal location. As such, the inflow will vary sinusoidally/cosinusoidally

## Slide 15: Peters-He (1989)
Excellent results in hover & forward flight
Good for aeroelastic analysis
More harmonics (up to 1,000) than Pitt-Peters
Final Year Project (FYP)
04/03/2020

## Slide 16: Vortex Ring State (VRS)
Flight regime: steep descents
Momentum theory breaks down=>
Invalid inflow assumptions=>
Unstable=> Challenge
Tip vortices approach rotor plane
Flapping, possible loss of control
Safety-critical flight condition
Final Year Project (FYP)
04/03/2020

## Slide 17: Vortex Ring State (VRS)
Final Year Project (FYP)
04/03/2020
Notes: ADD SOURCE.
CAN ALSO USE DR RIBERA THESIS’ PICTURES IF YOU WANT TO.

## Slide 18: Technical Note: Modification of Mass-Flow Parameter to Allow Smooth Transition between Helicopter and Windmill states (Peters & He, 2006 )
Modifies the mass flow parameter when transitioning from normal working state to VRS
Free wake data available to compare
Simple Peters-He extension
Clearly maps the VRS boundaries
Implemented using 3 equations
Final Year Project (FYP)
04/03/2020

## Slide 19: Technical Note: Modification of Mass-Flow Parameter to Allow Smooth Transition between Helicopter and Windmill states (Peters & He, 2006 )
Final Year Project (FYP)
04/03/2020
Notes: DO NOT EXPLIN THE MATHS IN a lot of detail. Do mention but no too much detail due to time.

## Slide 20: Progress
Reading about helicopter flight dynamics: 9/10
Reading & understanding about Pitt-Peters, Peters-He 10/10
Literature review of inflow models: 9/10
Selecting inflow model(s) to implement: 10/10
Learning FORTRAN: 7/10
Comparing inflow sub-routines to theory: 6/10
Implementing the model: To be Done
Final Year Project (FYP)
04/03/2020

## Slide 21: Next steps
Implement the Vortex Ring State inflow model
Produce plots such as the ones by Dr Ribera & Celi
Validate against the free wake data
Final Year Project (FYP)
04/03/2020
Notes: Could potentially try the ground effect one Although no validation available due to lack of existing flight test data nor the wake model (ground effect is not modelled for ground effect– This is one of the newest version of the wake model).
Have clear understanding of what the model and equations are, where they fit in. Not need to have started/finished coding. Be very clear about the direction/meaning of the project. TALK ABOUT THE CODE (flight dynamics code-introduction in Dr Ribera’s paper). WAHAT IT DOES AND DOES NOT DO. NOT A CFD CODE. HOW THE CODE CAN HAVE DIFFERENT CODES AND MODELS TO CALCULATE THESE VELOCITIES, FROM FREE WAKE TO DYNAMIC INFLOW. EXPLAIN HOW INFLOW FITS IN THERE. SAY ABOUT PROGRESS OF THE MODEL. EXTENDING FLIGHT CONDITIONS CAPTURED THROUGH THE INFLOW MODELS. IDEA: ADD LATER VERSIONS OF CODE. ESPECIALLY THE VORTEX RING STATE; ACCORDING TO DR RIBERAS THESIS. Highlight bits you want people to read.
Feedback: Take the subroutines I have been sent, and start looking at how to the equations in the model correlate with the code. Start to match that and see how it will match your own implementation. See how the commented bit matches any vortex ring corrections. Ensure you understand how the theory matches the 2 sub-routines.

## Slide 22: Timeline
March | Understanding inflow sub-routines Identifying which sub-routines to change Implementing the Vortex Ring criterion Coding the model(s)
April | Finish coding by mid-April Data analysis Report writing and data interpretation If time- 2nd model implementation
May | Report writing Data interpretation
Final Year Project (FYP)
04/03/2020
Notes: DO NOT SPEND TOO MUCH TIEM ON THIS.

## Slide 23: Thank you
End of Interim presentation
04/03/2020
Ioannis Karatsivoulis- Undergraduate Student, Department of Aeronautics, Imperial College London
Final Year Project (FYP)
04/03/2020